## Slide 1
time
Brett Barwick
Trinity College Physics Department
Hartford, CT
Imaging at the nanometer and femtosecond
scales with ultrafast electron microscopy

## Slide 2
Ultrafast electron microscopy at Trinity College
UEM in my lab is based on a point projection ultrafast electron microscope
Chosen for its simplicity, cost and flexibility

## Slide 3
At Caltech:
TEM~ $1 million
laser~ $500k
Lab ~ $1 million
Post docs, graduate students

## Slide 4
At Caltech:
At Trinity:
TEM~ $1 million
laser~ $500k
Lab ~ $1 million
Post docs, graduate students
Point projection/UEM
~$40k, homebuilt
laser ~ donated
Undergraduates

## Slide 5
Dispersion in UEM base on standard TEM:
Causes of temporal spread:
Space charge
Dispersion
Assuming no space charge how can we get around dispersion?
TEM

## Slide 6
Dispersion in UEM base on standard TEM:
Causes of temporal spread:
Space charge
Dispersion
Assuming no space charge how can we get around dispersion?
1) RF compression, already shown successful for UED in multiple groups
TEM

## Slide 7
Dispersion in UEM base on standard TEM:
Causes of temporal spread:
Space charge
Dispersion
Assuming no space charge how can we get around dispersion?
1) RF compression, already shown successful for UED in multiple groups
2) Optical/ponderomotive compression, should work in principle not demonstrated
TEM

## Slide 8
Dispersion in UEM base on standard TEM:
Causes of temporal spread:
Space charge
Dispersion
Assuming no space charge how can we get around dispersion?
1) RF compression, already shown successful for UED in multiple groups
2) Optical/ponderomotive compression, should work in principle not demonstrated
3) Don’t let the pulse have the time to disperse
TEM

## Slide 9
Length scales in TEM versus point projection EM:
~1 m
TEM
~10 µm
PPEM

## Slide 10
Modeling: Advantage of point projection versus
UEM base on standard TEM
- Standard UEM’s are limited – dispersion causes reduction in temporal resolution
- PPUEM, with tip very close to specimen can be one solution to this problem
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.

## Slide 11
Ultrafast nanometer tip sources have been shown to produce sub-cycle attosecond electron packets

## Slide 12
Current progress and device characterization
Our device:
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.

## Slide 13
Characterization: Imaging with photoelectrons
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.

## Slide 14
56 eV
photoelectrons
~80MHz,
~1 sec exposure
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.
Characterization: Imaging with photoelectrons

## Slide 15
Δt
Δt
single
pulse
double
pulse
tip
electron
detector
electron pulse
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.
Characterization: Emission time of electrons

## Slide 16
Δt
Δt
single
pulse
double
pulse
tip
electron
detector
electron pulse
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.
Characterization: Emission time of electrons

## Slide 17
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.
Characterization: Time of flight energy analysis
13 ns
Femtosecond laser pulses
2-D Electron
detector
Photodiode
Correlation
electronics

## Slide 18
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.
Characterization: Time of flight energy analysis
13 ns
Femtosecond laser pulses
2-D Electron
detector
Photodiode
Correlation
electronics
TOF spectra

## Slide 19
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.
Characterization: Time of flight energy analysis
13 ns
Femtosecond laser pulses
2-D Electron
detector
Photodiode
Correlation
electronics
TOF spectra
Simultaneously
obtain an image
-need a delay line
detector
camera

## Slide 20
Simulation: Sample spectra of photon induced near field spectra
25 eV electrons
pump laser of 800 nm
convoluted with detector resolution of 1 ns

## Slide 21
Current progress:
- Modeling shows very little dispersion in principle
- Imaging in pulsed mode with ~ 10 nm resolution
- TOF energy spectroscopy is demonstrated

## Slide 22
“Femtosecond photoelectron point projection microscope”,
Erik Quinonez, Jonathan Handali and Brett Barwick. Review of Scientific Instruments. 84, (2013) 103710.
Currently: Need to find “time zero”

## Slide 23
Currently: Need to find “time zero”
pump with tens of mJ/cm^2

## Slide 24
Currently: Need to find “time zero”
pump with tens of mJ/cm^2
Two main lasers in my lab
Oscillator, 80MHz, several nJ, 100 fs
Amplifier, 20Hz, 20 mJ, 100fs
Oscillator, enough electrons, not enough pump pulse energy
Amplifier, not enough electrons, plenty of pump pulse energy
  Need ~ 1 MHz, ~ 1 µJ and 100 fs or less for this method

## Slide 25
Currently: Need to find “time zero”
- Instead use oscillator and use local field enhanced fields due to optically excited plasmons
Image taken using photon induced near field electron microscopy
“Photon Induced Near-Field Electron Microscopy”
Nature, 462 (2009) 902-906.
Use enhanced field to deflect the electron pulses
Advantages:
- excitation can be pumped with an oscillator
- microscope has sufficient spatial resolution
- low energy electrons are very sensitive
- excited fields follow the optical field of the excitation laser

## Slide 26
metallic nanoparticle (d<<λ)
+
+
+
+
+
-
-
-
-
-
time t
time t+T/2
t
E
+
+
+
+
+
-
-
-
-
-
Future: Imaging attosecond dynamics at the nanoscale?
-attosecond PEEM is already at as and nm scales

## Slide 27
13 ns
Femtosecond laser pulses
2-D Electron
detector
Photodiode
Correlation
electronics

## Slide 28
“AMO” type experiments include
- Scalar AB effect
- Time-dependent decoherence effects
- Hanbury-Brown Twiss effect (or antibunching of electrons)
13 ns
Femtosecond laser pulses
Electron
detector
Photodiode
Correlation
electronics
Interaction region for experiments
Ultrafast low energy electron interferometry
Correlation
electronics
2-D Electron
detector

## Slide 29
Aharonov-Bohm effect
Two AB effects:
Magnetic (vector) and electric (scalar)
-Tonomura completed experiments demonstrating the magnetic AB version
-To date no attempts of electric version
-Needs pulsed electron source!

## Slide 30
Future: TEM based UEM at Trinity?

## Slide 31
This work was supported by FRC, Trinity Startup Funds and CT Space Grant, and special thanks to Prof. Ahmed Zewail for donation of the laser system.
Trinity Students that have worked on
these projects:
Jonathan D. Handali, 2013
Erik Quinonez, 2014
Bhola Uprety, 2014
Pratistha Shakya, 2015
Abhishek Khanal, 2015

## Slide 32
d1
d2
e- detector
e- tip source
fs e- excitation
pulse
fs electron pulse
specimen
fs specimen
excitation
pulse
Ultrafast Electron Point
Projection Microscope
Typical image achieved
in an e- point projection
microscope of carbon
fibers, adapted from
reference [5].
-V