## Slide 1
X-band Deflectors for Femtosecond Diagnostics of Electron Beams
V.A. Dolgashev,
SLAC National Accelerator Laboratory
10 December, 2013
FEIS 2013 - Femtosecond Electron Imaging and Spectroscopy
Key West, Florida,
December 9 - 12, 2013

## Slide 2: Acknowledgments
I want to thank all contributors to this report:
Gordon Bowden, Yuantao Ding, Paul Emma, Patrick Krejcik, James Lewandowski, Cecile Limborg, Michael Litos, Robert Reed, Juwen Wang, and Dao Xiang of SLAC
Joel England of SLAC and previously of UCLA
Pietro Musumeci of UCLA
Jake Haimson of Haimson Research Corporation
Alex Murokh and Luigi Faillace of Radiabeam Technologies
Craig Wilsen of L3 Communications

## Slide 3: Outline
Introduction
Traveling wave (TW) rf deflectors
  SLAC 11.4 GHz deflectors
  Radiabeam Tech. 11.4 GHz TW deflector for BNL Accelerator Test Facility (BNL-ATF)
Standing wave (SW) deflectors
  UCLA 9.6 GHz deflector
  Hiamson Research 17 GHz circularly polarized deflector
  Radiabeam Tech. deflector for Ultrafast-Electron-Diffraction
New X-band rf power sources and configurations

## Slide 4: Introduction
Why X-band for rf deflectors?
Compact
Practical devices that allow extreme timing resolution, such as ~10 fs at 14 GeV
Practical way to build portable ~fs beam diagnostics for ~MeV beams
Difficulty:
Need expensive rf power sources, from kilowatts to 10th MW of X-band rf power

## Slide 5
Frequency | 11.424 GHz
Beam pipe diameter | 10 mm
Phase advance per cell | 2π/3
Kick per meter | 31 MeV/m/Sqrt(20 MW)
115 cell +2 matching cells structure kick | 24 MeV/Sqrt(20 MV)
Maximum Electric field (input coupler) | 100 MV/m / Sqrt(20 MW)
Maximum Magnetic field (input coupler) | 400 kA/m / Sqrt(20 MW)
Group velocity/ speed of light | 3.2 %
Structure length (with beam pipes) | ~1.2 m
11.424 GHz Traveling Wave Deflector for LCLS
J. Wang et al., SLAC
1.2 m

## Slide 6: Regular Cell, HFSS Model
J. Wang et al., SLAC
10 mm

## Slide 7: Periodic 2Pi/3 traveling wave deflector, 20 MW, deflecting gradient 31 MV/m
Maximum surface electric fields 86 MV/m.
Maximum surface magnetic fields 340 kA/m,
Pulse heating 16 deg. C for 100 ns pulse.
a = 5 mm
t = 2 mm, round iris
Q=6,300
working mode
parasitic mode, ~100 MHz separation

## Slide 8
J. Wang et al., SLAC

## Slide 9: Waveguide Coupler for TW X-band Deflector, 20 MW of Transmitted Power, or 21.3 MeV kick for 89 cm structure
Maximum surface electric fields ~100 MV/m.
Maximum surface magnetic fields ~400 kA/m,
Pulse heating 22 deg. C for 100 ns pulse.
V. Dolgashev, “Waveguide coupler for x-band defectors,” Presented at Advanced Accelerator Concepts Workshop 2008, SLAC-WP-084, Santa Cruz, CA, (July 27 – August 2, 2008).

## Slide 10
Input/Output Couple Assemblies
Completed Couple Assembly
Mechanical Design Model (Robert Reed)
J. Wang et al., SLAC

## Slide 11: P. Emma, An X-Band Transverse RF Deflector for the LCLS, Oct. 18, 2006
Table 1. Parameters for a 10-fs temporal resolution using an X-band RF deflecting cavity.
Parameter | symbol | value | unit
Electron energy | E | 13.6 | GeV
Desired temporal resolution | Dt | 10 | fs
Offset of Dt-particle on screen, in units of rms beam size | n | 2 | 
RF wavelength of deflector (X-band) | l | 26 | mm
Vertical normalized rms emittance | eN | 1 | mm
Vertical beta function at the center of the RF deflector | bd | 50 | m
Peak vertically accelerating voltage seen by beam | V | 33 | MV
Table 3. Approximate specifications for an X-band RF deflecting cavity.
Parameter | symbol | value | unit
Maximum repetition rate | f | 120 | Hz
Minimum iris radius (if located after undulator) | r | 5 | mm
Maximum cavity length (approx.) | L | 2 | m
Minimum RF pulse length | DtRF | 100 | ns
RF frequency | fRF | 11.424 | GHz
RF phase stability at f > 1 Hz (rms) | jrms | 0.05 | deg-X
RF relative amplitude stability (rms) | DV/V0 | 1 | %
SLAC XL-4 Klystron, 50 MW, <1.6 us
3 dB splitter
20 MW
100 ns
20 MW
100 ns
bunch
~190 cm
Kick
48 MeV
13.6 GeV
Application: 10 fs Time Resolution for 13.6 GeV LCLS Beam

## Slide 12: XTCAV: x-ray beams temporal diagnostics
Screen, FEL ON
Screen, FEL OFF
time
e-
sz
2×1 m
bd
bs
D  90°
V(t)
RF
‘streak’
Dipole
X-band TCAV
energy
Dy
XTCAV for x-ray temporal diagnostics:
High resolution, ~ few fs;
Applicable in all FEL wavelength;
Wide range, ~ 1 fs to ~100s fs;
Beam profiles, single shot;
No interruption with operation;
Both e-beam and x-ray profiles.
Project started in 2011, and took about two years to complete, total cost ~$5M,
and now routine diagnostics
XTCAV streaks horizontally;
Dipole bends vertically.
Reconstruction e-beam profile
Reconstruction x-ray profile
Y. Ding et al., Phys. Rev. STAB.14.120701 (2011)
P. Krejcik et al., in Proceedings of IBIC2013 (Oxford, UK)

## Slide 13
1-meter-long X-band deflector at FACET
M. Litos at al., SLAC

## Slide 14
X-Band Transverse Deflecting Structure at FACET
Beam energy 20 GeV
1-meter-log deflector with 25 MeV kick
Installed in FACET beamline in May 2012
Commissioning began 1st June 2012
Practical resolution: ~70 fs
First image of two-bunch structure 6/5/12
deflection
dispersion
M. Litos at al., SLAC
M. Litos, M. Bionta, V. Dolgashev, R. England, D. Fritz, S. Gilevich, P. Hering, and M. Hogan, in Proceedings of the PAC2011 (New York, USA, 2011).

## Slide 15
Two Short Traveling Wave X-Band Deflectors for SLAC Next Linear Collider Test Accelerator (NLCTA)
J. Wang et al., SLAC
11-cell
27-cell

## Slide 16
Beapull measurements of 27-cell deflector
Juwen Wang, “RF Deflector Developments and Applications at SLAC,” SLAC Accelerator Seminar, April 12 2011
X-band deflector at SLAC NLCTA,
~6MV kick at 20 MW, time resolution ~30 fs at 100 MeV
Dao Xiang et al., SLAC
~4 ps
~ 3 MeV

## Slide 17
11-cell deflector installed in beamline
C. Limborg et al., in Proceedings of HBEB2013 (Puerto Rico, US, 2013).
Cecile Limborg, SLAC
X-band deflector installed at SLAC X-Band Test Area, ~1MV kick at 2 MW of RF,
time resolution ~30 fs at 100 MeV

## Slide 18: 11.424 GHz Traveling Wave Deflector by Radiabeam Technologies
Frequency | 11.424 GHz
Beam pipe diameter | 10 mm
Phase advance per cell | 2π/3
Kick per meter | 38 MeV/m/Sqrt(20 MW)
53 cell structure kick | 15 MeV/Sqrt(20 MV)
Maximum Electric field (first regular cell) | 92 MV/m/Sqrt(20 MW)
Maximum Magnetic field (first regular cell) | 345 kA/m/Sqrt(20 MW)
Group velocity/ speed of light | 2.7 %
Structure length | ~46 cm
A . Murokh et al., Design and Fabrication of an X-band Traveling Wave deflection Mode Cavity for Longitudinal Characterization of Ultra-Short Electron Beam Pulses, Proc. Of EPAC08, Genoa, Italy, 2008, pp. 1215-1217
A. Murokh, Radiabeam Tech.

## Slide 19: Manufacturing
Adapted SLAC cleaning and handling procedures developed for high gradient X-band structures
A. Murokh, Radiabeam Tech.

## Slide 20
Complete deflector,
Now at BNL waiting for high-power tests
Luigi Faillace, Radiabeam Tech.

## Slide 21
Cold Measurements,
done at SLAC on September 2012
L. Faillace, Radiabeam Tech.
Reflection
Transmission
On-Axis Electric Field
Bead pull measurements , reflection from bead
R. Agustsson et al. in Proceedings of IPAC2012 (New Orleans, Louisiana, USA, 2012) pp. 3389–3391

## Slide 22: Proposed application: Measurements of Longitudinal Phase Space of BNL ATF Beam
Longitudinal resolution should be better than 10 fs for beam energy 75 MeV and transverse emittance ~2 um.
100 fs
Numerical (ELEGANT) model of ATF X-band deflector experiment: a post-compressor beam longitudinal phase space in (p,t)-coordinates
(X,Y) map after the rf deflector and a bending magnet
A . Murokh, Radiabeam Tech.

## Slide 23
9.3 GHz SW deflector at UCLA
Frequency | 9.6 GHz
Beam pipe diameter | 10 mm
Phase advance per cell | π
9 cell structure kick | 0.528 MeV/Sqrt(50 kW)
Unloaded Q | 13043
External Q | 13517
Structure length (without beam pipes) | ~14 cm
R. J. England et al., X-Band Dipole Mode Deflecting Cavity for the UCLA Neptune Beamline, in Proc. of PAC 2005 , Knoxville, Tennessee
R. J. England, SLAC/UCLA

## Slide 24: Cavity Design
reconditioned VA-24G X-band klystron (50 kW peak)
one cell with polarization holes
9-cell standing wave structure made of GlidCop
cells are stacked ConFlat vacuum flanges – no brazing
center-fed input rf
EDM’ed polarization holes
R. J. England, SLAC/UCLA

## Slide 25: Application: Measurement of Longitudinal Phase Space
P. Musumeci, UCLA

## Slide 26
Measurements of 3.5 MeV beam:
  Time resolution is 50 fs
  Energy resolution is 1 keV, determined by energy spread introduced by rf deflector
Very linear phase space
High 6D beam brightness
Ultralow longitudinal emittance (<0.5 um)
Longitudinal phase space measurement compared with simulation. Bunch charge 20pC, 500 micron rms laser spot size on the cathode.
P. Musumeci, UCLA
Application: Measurement of Longitudinal Phase Space
J. T. Moody et al., Longitudinal phase space characterization of the blow-out regime of rf photoinjector operation, Phys. Rev. STAB 12, 070704 (2009)

## Slide 27: Ultrafast relativistic electron diffraction with RF streak camera
Truly single shot technique
Temporal resolution set by RF deflector and not limited by e-beam bunch length or time-of-arrival jitter
P. Musumeci, UCLA

## Slide 28: Ultrafast relativistic electron diffraction with RF streak camera, Single shot study of heating and melting of gold crystal
P. Musumeci et al. Journal of Applied
Physics, 108, 114513 (2010)
(200)
(220)
(200)
(220)
Capturing ultrafast structural evolutions with a single pulse of MeV electrons:
RF streak camera based electron diffraction.
These are obtained by moving the mechanical delay line
Results in excellent agreement with
frame-by-frame UED experiment

## Slide 29
x
t
Streaked Electron radiography:
Single shot study of Electro-Magnetic field dynamics
1
2
P. Musumeci, UCLA
C.M. Scoby et al., Single-shot 35 fs temporal resolution electron shadowgraphy,
Appl. Phys. Lett., 102, 023506, (2013)

## Slide 30
RF deflector self-calibration
Maximize resolution by using quadrupoles and increasing screen distance
Expansion of space-charge hole way too fast to be related to actual electron-cloud expansion
38 fs rms
Turn pump laser on
500 fs
150 um
c
P. Musumeci, UCLA

## Slide 31: 17 GHz circularly polarized SW deflector by Haimson Research Corporation
Frequency | 17.136 GHz
Beam pipe diameter | 4.96 mm
One polarization kick | 0.42 MeV/Sqrt(734 kW per cavity)
Unloaded Q | 3500
External Q | 3500
Maximum electric field | 89 MV/m/Sqrt(734 kW per cavity)
Maximum magnetic field | 204 kA/m/Sqrt(734 kW per cavity)
J. Haimson, Haimson Research Corporation
Advanced Accelerator Concepts, AIP Conference Proceedings, 647, (New York: AIP Press, 2002) , pp. 810-820
Advanced Accelerator Concepts , AIP Conference Proceedings, 737, (New York: AIP Press, 2004), pp. 95-108

## Slide 32
J. Haimson, Haimson Research Corporation
S-Band RF Bunch Measurements Using a Circularly Scanned Beam (2 x TE102 Rectangular Cavities With Transverse Magnetic Fields)
J. Haimson, High Current Traveling Wave Electron Linear Accelerators, In Proc. of PAC 1965, Washington DC, March 1965, pp. 996-1011
J. Haimson, Optimization Criteria for Standing Wave Transverse Magnetic Deflection Cavities, Proc. of 1966 Linear Accelerator Conference, LA-3609, Los Alamos, 1966, pp. 303-331.
Method

## Slide 33
17 GHz Circularly Polarized RF Deflector Designed for Displaying the Longitudinal Phase Space of 1 Degree Electron Bunches from a 17.136 GHz 15 MeV Linac
J. Haimson, Haimson Research Corporation

## Slide 34
Typical electron bunch longitudinal phase space displays obtained with near optimum chopper-prebuncher operation of the 17 GHz linac, showing the energy and phase charge distributions as the injector controls were adjusted to reduce the bunch length by a factor of 5.
Application: Measurement of Longitudinal Phase Space
J. Haimson, Haimson Research Corporation
1o@17 GHz =162 fs

## Slide 35
Application: Measurement of Longitudinal Phase Space
15 MeV, 1.7° Linac Bunch After Circularly Polarized Deflection and Transmission Through a Matrix of Precision Collimators
J. Haimson, Haimson Research Corporation

## Slide 36
9.3 GHz SW deflector for streaked Ultrafast Electron Diffraction by Radiabeam Technologies
Frequency | 9.3 GHz
Beam pipe diameter | 5.6 mm
Phase advance per cell | π
3 cell structure kick | 0.02 MeV/Sqrt(1 kW)
Unloaded Q | 9,200
External Q | 9,200
Structure length (without beam pipes) | ~9 cm
Luigi Faillace, Radiabeam
Input RF
coupler
Nose cone type cells
Side cell
Inter-cell
coupling slot
L. Faillace et al., THPPC048 Proceedings of IPAC2012, New Orleans, Louisiana, USA

## Slide 37: Side-Coupled Cavity with Nose-Cones
Use of nose-cone in the cavities is a practical solution for low-beta (β=0.54) deflector.
Luigi Faillace, Radiabem
Number of cavity cells
vs. available RF power

## Slide 38
Streaked Ultrafast Electron Diffraction System
Electron Energy | 100 keV
Number of electrons/pulse | 107
Pulse Length (at the sample) | 20 ps
Deflector RF power | 1 kW
Deflector Nominal Voltage | 20 kV
Temporal Resolution of System | 30 fs
Pump laser
pulse
Diffracted
e- bunch
Main Parameters
Originally proposed by P. Musumeci et al., Review of Scientific Instruments (2009) vol. 80 pp. 013302
Luigi Faillace, Radiabem

## Slide 39
Prospective use of new commercial
X-band RF Sources for deflector
applications

## Slide 40: Recently advertised commercial 9.3 GHz klystrons
Parameter | Units | CPI-VKX-7993 | L3-L-6145
Focusing |  | PPM | Solenoid
Frequency | GHz | 9.3 | 9.3
Peak Power | MW | 2.7 | 5
Average Power | kW | 5.4 | 20
Efficiency | % | 43 | 47
Saturated Gain | dB | 53 | 47
Bandwidth (-1 dB ) | MHz | 65 | >40MHz
Beam Voltage | kV | 120 | 130
Duty factor | % | 0.2 | 0.4
Beam Current | A | 52 | 83
A. Balkcum et al., Design and Operation of a 2.5 MW, PPM Focused X-Band klystron, In Proc. of IEEE International Vacuum Electronics Conference, Rome, Italy, April 28-30, 2009
Mark Kirshner et al., High Power X-Band Klystron, In Proc. of IEEE International Vacuum Electronics Conference, Rome, Italy, April 28-30, 2009
CPI-VKX-7993
L3-L-6145

## Slide 41
L6145, 6 MW
3 dB splitter
3 MW
150 ns
3 MW
150 ns
bunch
~300 cm
Kick
20 MeV
L6145, 6 MW
3 dB splitter
6 MW
150 ns
6 MW
150 ns
bunch
~300 cm
Kick
28 MeV
SLED pulse
compressor
12 MW
150 ns
V.A. Dolgashev, SLAC, 2 October 2013
1st stage
2nd stage, added SLED
6 MW,
150 ns
6 MW,
2000 ns
Possible deflector configurations powered by 9.3 GHz, 6 MW klystron for diagnostics of GeV beams

## Slide 42
Standing Wave Deflector for ~10 fs diagnostics of MeV beams
Valery Dolgashev , “Waveguide Coupler for X-Band Deflectors,” SLAC-WP-084, AAC08, Santa Cruz, California, 27 Jul - 2 Aug 2008.

## Slide 43: Waveguide coupler for 6 cell SW X-band deflector, 1.5 MW of input power, deflection 2 MeV
Maximum surface electric fields ~105 MV/m.
Maximum surface magnetic fields ~420 kA/m,
Pulse heating 24 deg. C for 100 ns pulse.

## Slide 44: Parameters of 6 cell X-band SW deflector
Frequency | 11.424 GHz
Beam pipe diameter | 10 mm
One cell length | 13.121 mm
Phase advance per cell | π
One cell kick | 0.34 MeV/Sqrt(0.25 MW)
Structure kick (6 cells) | 2 MeV/Sqrt(1.5 MW)
Unloaded Q | 7800
Loaded Q | 3800
Maximum Electric field | 105 MV/m / Sqrt(1.5 MW)
Maximum Magnetic field | 420 (kA/m) / Sqrt(1.5 MW)
Structure length (with beam pipes) | 12 cm
Near mode separation | 13.6 MHz

## Slide 45: Estimation of resolution
See for example, P. Emma, J. Frisch, P. Krejcik, LCLS-TN-00-12, Aug. 2000.

## Slide 46
Variable splitter
20 MW, 0.2 us
Schematic of rf high gradient streak camera with ~10fs resolution based on a commercial X-band klystron
SLED pulse
compressor
Phase shifter
φ
or
Klystron L3-L-6145, 9.3 GHz, 5 MW, 3 us
5…15 MW, 0.2 us
2…5 MW,
0.2 us
X-band RF gun
Lens
Vertical
rf deflector
φ
Horizontal
rf deflector
Variable splitter
5 MW, 3 us
2 MeV x 2 MeV
kick
4-10 MeV
~3 m
Screen

## Slide 47
Summary
X-band deflectors are used femtosecond beam diagnostics in accelerators and novel methods in ultrafast physics.
Development of new rf deflectors utilizes mature high gradient X-band technology.
Introduction of commercial X-band klystrons opens new possibilities for practical applications of the rf deflectors: for example a steak camera that will improve the state-of-the-art time resolution by an order of magnitude or better.